| Gigaset C470 Gigaset C475 Convenience with a pleasing touch |  |
| --- | --- |
| Interface: a/b (analogue) Operation: HA / PBX Standards: DECT, GAP, F-SMS Configuration Connection of 1 external line Up to 6 handsets can be registered Handset for up to 4 base stations Main Features |  |
| Design Slim, modern handset design Modern L-shape base design Cradle in base Base and charger wall mountable Easy to use product concept Plug and play Automatic handset registration (place handset in base and registration is performed automatically) Automatic SMS registration Comfortable time and date setting (initial installation; buffered in case of power loss) Comfortable dial and text editors Comfortable menu with colored icons and text for easy use in 20 languages (partly available) Illuminated color display and keypad (amber) Softkey with 4 pressure points for special applications Red illuminated MWI and Handsfree key Flash-key (R) with longpress for pause (P) 4 way Navikey ECO DECT Up to 60% less electricity consumption in comparison with conventional power supplies by switched mode power supply Reduction of transmitting power to almost zero when handset is docked automatical at registration of 1 handset Reduction of transmitting power of the base manual reduction of transmitting power of base station by 80% if more than 1 handsets are registered (approx. splitting the range) Handset reduces the transmitting power automatically depending on the distance to the base | Color-Display Illuminated 6 line graphical color handset display (128x128 pixel, 4096 colors) Standby Display of digital clock or color picture as screensaver (4 choices, settable by user) Date and time, state of charging and signal strength, handset name displayed During Connection Display of call duration Directory Directory with up to 150 numbers and names VIP-entries (a specific melody can be assigned to each directory entry) Handsfree Speaking / Headset / Earpiece Enhanced handsfree speaking with superior sound quality, separate speaker activated by illuminated Handsfree-key, volume adjustable (5 volume steps) Headset connection (mono) via 2,5mm jack connector (headset not included) Adjustable handset earpiece volume (3 levels) Melodies 5 polyphonic sounds and 10 melodies (composed by musician) 5 loudness levels + off + crescendo Selectable internal call melody Dialing Big dialing font (22pt) Dial preparation with correction possibility by entering the phone number before connecting the line Redialing list for up to 20 different numbers; start via send button Speed-dialing using keys 2 – 9, 0 (shortcut) Automatic prefix dialing of network provider Dial mode: tone, pulse |
| Receiving Calls CLIP and CNIP displayed 1) 2) Display and handsfree key lighted Ringer animation in display Ringer output - in handset by handsfree speaker - in AM base by AM speaker Missed calls Illuminated MWI-key signaling new messages with comfortable access to message list Call log list or Missed call list saving calls with CLIP / CNIP (approx. 30 entries, base required, factory setting) 1) Missed call notification via SMS to external number 1) 2) Additional features Alarm clock functionality with snooze function Keypad lock; protection from unintentional usage Baby-Alarm / room monitoring Editable internal handset name Support of Netprovider features via menu 1) 2) Additional features with accessories Headset via 2,5mm jack connector VoIP - Speaking on the phone over Internet via dedicated accessory or base unit Gigaset Home Control (GHC) - protocol for the operation of DECT modules SMS & Email 1) 2) Automatic SMS registration Sending and receiving of SMS with up to 612 characters Storage of up to 30 SMS with 90 digits Up to 4 personalized SMS-Inboxes2) Comfortable access to SMS-Services (info-channels) 2) Transmission of e-mails via SMS 1) 2) Copy of telephone numbers from SMS to directory V-Card support: name and number can be taken over to directory Features with more than 1 handset 3 calls simultaneously (1 external/2 internal) Transfer of external calls to another handset with prior consultation call or recall Collective internal call in case of incoming external calls 3 party conference (1 external/2 internal participants) Directory transfer between handsets | Features of the integrated answering machine Digital recording of voice messages with up to 40 minutes recording time Simple usage via handset and keys on base station Predefined announcement (plug & play) 1 Individual announcement and 1 advisory announcement (170 Sec.) recordable by user Time-controlled change between announcement and advisory message Recording date and time are announced Recording time adjustable: unlimited, 1/ 2/ 3 minutes Call acceptance adjustable: immediately, automatic, after 10, 18, 30 Sec. Display of new messages at the handset New message notification via SMS to external number containing CLIP, date, time 1) 2) Remote listening of messages via - PIN-protected remote playback - SMS initiated call-back from AM 1) 2) Live recording of a telephone call Recordings have unlimited protection against power failure |
| Technical data Handset Standby-time: up to 300 hours Talk time: up to 12 hours Battery: 2 x NiMH AAA Indoor range: up to 50 meters Outdoor range: up to 300 meters Registration: at 1 base station Dimensions: Length 28 mm Width 48 mm Height 146 mm Base station Connection of 1 external line Connection of up to 6 handsets Charging cradle in base unit Paging key on front of base Operation of AM through keys on AM base Dimensions Base: Length 66 mm Width 121 mm Height 93 mm AM Base: Length 72 mm Width 143 mm Height 93 mm Colour: black Package contents 1 Handset 1 Belt clip 1 Base station 2 AAA batteries 1 energy saving swichmode power supply unit 1 Telephone cord 1 User manual 1) Country / customer specific 2) Provider dependant 3) Handset standing, handset an base orientation front Length = front <-> back Width = left <-> right Height = top <-> bottom Remarks Base and cradle wall mountable call by call key, pre-programmable with service numbers Easy Text-Input-Method to help writing SMS (EATONI) available upon request |  |

# Authors

| Name | Org. | Tel. | E-Mail |
| --- | --- | --- | --- |
| Daniela Barthel | SHC PM P PD | +49-89-722-34669 | daniela.barthel@siemens.com |
| Tanja Yusuf | SHC PM CV | +49-89-722-58625 | tanja.yusuf@siemens.com |
| Igor Jejina | SHC PM CV | +49-89-722-40171 | Igor.Jejina@siemens.com |
| Karl Fleischer | SHC PM PS | +49-89-722-33369 | fleischer.karl@siemens.com |

Copyright  Siemens Home and Office Communication GmbH & Co. KG 2006

Copying of this document and giving it to others and the use or communication of the contents thereof, are forbidden without express authority. Offenders are liable to the payment of damages. All rights reserved in the event of the grant of a patent or the registration of a utility model or design.

# History of Change

| Version | Date | Author(s) | Remarks |
| --- | --- | --- | --- |
| 1.0 | 12.06.06 | Daniela Barthel | M0 Version created |
| 1.1 | 18.08.06 | Tanja Yusuf | M1 draft version created |
| 1.2 | 14.09.06 | Tanja Yusuf | M1 version created: - 140 directory entries |
| 1.3 | 14.11.06 | I. Jejina / T. Yusuf | M1 Update: - document structure adapted - Official naming added - Changed to single base concept - 150 directory entries possible - Birthday reminder deleted - Sending and receiving of SMS with up to 612 characters (instead of 160) - V-card support added - Recording time increased to 40 minutes - Adjustable recording time changed to: unlimited, 1/ 2/ 3 minutes - Dimensions added - Only one color: black |
| 1.4 | 08.12.06 | T. Yusuf | - Picture with corrected naming and picture of AM-version added - Bigger font for dialling preparation (22pt) added - SMS: personalized Inboxes / Services added - Increased recording time: up to 40 minutes - Call acceptance adjustable: after 10, 20, 30 Sec |
| 1.5 | 15.12.2006 | T. Yusuf | - Base and charger wall-mountable added - Chapter Eco-Dect added |
| 1.6 | 02.03.2007 | K. Fleischer | - 4 Screensaver - call acceptance 18 Sec. - talk time up to 12 hours (R-Team 28.02.07) - standby-time: up to 300 hours |
| 1.7 | 12.10.2007 | K. Fleischer | -handset for up to 4 base stations -Softkey with 4 pressure points for special applications - Eco-DECT - color display - pictures actualized - energy saving swichmode power supply unit |
| 1.8 | 23.11.2007 | K. Fleischer | ECO-DECT: almost zero |